RV  CONDITION INSPECTION

| OWNER | A/C TYPE | DATE |
| --- | --- | --- |
| SER. NO. | N NUMBER | MANUFACT. DATE |
| TYPE INSPECTION | TACH TIME | TOTAL A/C TIME |

| PROP. GROUP |  |  | INSP. |
| --- | --- | --- | --- |
|  | 1 | REMOVE SPINNER, INSPECT BULKHEADS FOR DEFECTS, CRACKS, LOOSE / SMOKING RIVETS |  |
|  | 2 | INSPECT BLADES FOR SECURITY, NICKS, CRACKS OR OTHER DAMAGE |  |
|  | 3 | INSPECT PROP HUB FOR EVIDENCE OF DAMAGE, CRACKS OR CORROSION |  |
|  | 4 | CHECK ALL MOUNT HARWARE FOR DEFECTS AND SECURITY |  |
|  | 5 | CHECK ATTACH BOLTS FOR TORQUE / SAFETY WIRE |  |
|  | 6 | CONSTANT SPEED |  |
|  |  | CHECK BLADES FOR TIGHTNESS IN HUB |  |
|  |  | REMOVE PROP, REMOVE SLUDGE (IF REQUIRED) |  |
|  |  | LUBRICATE AS PER MANUAL |  |
|  |  | INSPECT COMPLETE ASSEMBLY |  |
|  | 7 | RE-INSTALL SPINNER |  |
| ENGINE GROUP |  |  |  |
|  | 1 | REMOVE ENGINE COWLS |  |
|  | 2 | CLEAN ENGINE AND COWLS |  |
|  | 3 | COMPRESSION TEST /80 HOT_______COLD______1_____2._____3._____4._____ |  |
|  | 4 | DRAIN ENGINE OIL (WARM) |  |
|  | 5 | REMOVE AND INSPECT OIL SUMP SCREEN FOR DEBRIS |  |
|  | 6 | REPLACE OIL FILTER, CUT OPEN AND INSPECT FILTER FOR DEBRIS |  |
|  | 7 | CHECK OIL SENDER UNIT FOR LEAKS AND SECURITY |  |
|  | 8 | CLEAN AND CHECK OIL COOLER FOR CRACKS AND SECURITY |  |
|  | 9 | CHECK OIL COOLER MOUNTINGS & BAFFLES FOR CRACKS AND SECURITY |  |
|  | 10 | CHECK AND CLEAN FUEL FILTER, GASCOLATOR, OR SCREENS |  |
|  | 11 | INSPECT FUEL INJECTOR LINES / NOZZELS FOR DEFECTS AND SECURITY |  |
|  | 12 | CHECK FUEL SYSTEM FOR EVIDENCE OF LEAKAGE, DETERIORATION, SECURITY |  |
|  | 13 | CHECK FUEL PUMP INLET/OUTLET FITTINGS ARE TIGHT AND SECURE |  |
|  | 14 | CHECK FUEL LINES FOR AGE, DETERIORATION, LEAKS AND SECURITY |  |
|  | 15 | CHECK ALL OIL LINES FOR AGE, DETERIORATION, LEAKS AND SECURITY |  |
|  | 16 | SERVICE / REPLACE AIR FILTER, INPECT AIRBOX FOR CRACKS, SECURITY |  |
|  | 17 | CHECK CARB HEAT AND CONTROLS FOR PROPER OPERATION AND SECURITY |  |
|  | 18 | CHECK MAGS FOR PROPER INSTALLATION, SECURITY AND OIL LEAKAGE |  |
|  | 19 | REMOVE / INSTALL MAG FOR 500 HR CHECK IF REQUIRED |  |
|  | 20 | CHECK CARB / FUEL INJECTION INLET SCREENS, DRAIN CARB BOWL |  |
|  | 21 | CHECK / ADJUST MAG TIMING LEFT______RIGHT______ |  |
|  | 22 | CHECK IGNITION HARNESS AND INSULATORS, P-LEADS FOR SECURITY |  |
|  | 23 | SERVICE OR REPLACE SPARK PLUGS |  |
|  | 24 | CHECK CONDITION OF ALTERNATOR, BELT AND WIRING, CHECK BELT TENSION |  |
|  | 25 | CHECK CONDITION OF STARTER AND CONNECTIONS |  |
|  | 26 | INSPECT EXHAUST SYSTEM FOR LEAKS, MOUNTS FOR SECURITY, CRACKS, TORQUE |  |
|  | 27 | INSPECT MUFFLERS, HEAT SHROUD, SCAT TUBING |  |
|  | 28 | CHECK ENGINE BAFFLES AND BAFFLE ATTACHMENTS |  |
|  | 29 | CHECK BREATHER TUBE FOR OBSTRUCTIONS, SECURITY |  |
|  | 30 | CHECK CRANKCSE FOR LEAKS, CRACKS, LOOSE FASTENERS, ETC. |  |
|  | 31 | CHECK ENGINE MOUNTS FOR SECURITY, CHECK FIREWALL ATTACHMENT NUTS/BOLTS |  |
|  | 32 | CHECK ENGINE MOUNT BUSHINGS FOR DETERIORATION |  |
|  | 33 | CHECK FIREWALL SEALS |  |
|  | 34 | CHECK THROTTLE, MIXTURE, ALTERNATE AIR, PROP CONTROLS FOR SECURITY AND PROPER OPERATION. INSPECT ALL ATTACH HARDWARE FOR SECURITY |  |
|  | 35 | CHECK ALL INLET CLAMPS, GASKETS AND INLET TUBE BOLT TORQUE |  |
|  | 36 | FILL ENGINE OIL..TYPE_________________QUARTS________ |  |
|  | 38 | LUBRICATE ENGINE CONTROLS |  |
|  | 39 | CHECK BATTERY TERMINALS ARE TIGHT, CLEAN. CABLES FOR DAMAGE, SECURITY |  |
|  | 40 | CHECK PUSHROD SHROUNDS - ECI PUSHROD RETAINER CLIPS – REPLACE IF NEC |  |
|  | 41 | PERFORM FUEL FLOW TEST AS REQUIRED (30 GPH / 200HP) |  |
|  | 42 | CHECK ENGINE GROUND CABLES FOR ATTACHMENT AND SECURITY |  |
| CABIN GROUP |  |  |  |
|  | 1. | INSPECT CANOPY HINGES, STRUTS, LATCHES, LOCKING MECHANISM, OPERATION |  |
|  | 2. | INSPECT CANOPY FRAME AND GLASS FOR GENERAL CONDITON |  |
|  | 3. | CHECK SEAT, SEAT BELTS, ATTACHMENTS AND BOLTS |  |
|  | 4. | CHECK ELEVATOR AND AILERON TRIM OPERATION |  |
|  | 5. | CHECK FUEL ON-OFF VALVE FOR PROPER OPERATION AND MARKING |  |
|  | 6. | CHECK FUEL SYSTEM LINES, PUMP, B-NUTS FOR SECURITY, CHAFING, LEAKS. REMOVE FUEL FILTER AND CLEAN. CHECK FOR LEAKS (PUMP ON) |  |
|  | 7. | CHECK OPERATION OF INTERIOR LIGHTING |  |
|  | 8. | CHECK RUDDER PEDALS, CABLES, CHECK TUBES AND PEDALS FOR CRACKS, SECURITY |  |
|  | 9. | CHECK CONTROL STICK,BEARINGS, PUSHRODS FOR OPERATION AND SECURITY |  |
|  | 10 | CHECK INSTRUMENTS, LINES, WIRES FOR PROPER INSTALLATION AND SECURITY |  |
|  | 11 | CHECK ALTIMETER / TRANSPONDER CERTIFICATION DATE |  |
|  | 12 | CHECK MASTER CYLINDERS FOR PROPER INSTALLATION, LEAKS, SECURITY |  |
|  | 13 | CHECK CONTROL STICKS, BOLTS, JAM NUTS, TORQUE TUBES FOR PROPER INSTALLTION AND SECURITY. LUBRICATE ALL BEARINGS AND BUSHINGS. |  |
| FUSELAGE GROUP |  |  |  |
|  | 1. | REMOVE ALL INSPECTION PANELS INCLUDING TAIL FAIRINGS |  |
|  | 2. | CHECK GENERAL CONDITION OF SKIN |  |
|  | 3. | REMOVE BAGGAGE COMPARTMENT COVERS AND BULKHEADS |  |
|  | 4. | CHECK WIRING, HOSES, ETC. FOR DAMAGE AND SECURITY |  |
|  | 5. | CHECK ANTENNA WIRES AND CONNECTIONS |  |
|  | 6. | CHECK AND SERVICE E.L.T. BATTERY GOOD UNTIL___________________ |  |
|  | 7. | CHECK BULKHEADS AND STRINGERS FOR DAMAGE |  |
|  | 8. | CHECK WING SPAR ATTACH BOLTS (MAIN AND AFT SPAR) FOR PROPER TORQUE |  |
|  | 9. | CHECK EMPENNAGE SURFACES FOR DAMAGE |  |
|  | 10 | CHECK RUDDER HINGES, HORN, AND ATTACHMENTS |  |
|  | 11 | CHECK VERTICAL FIN ATTACHMENTS |  |
|  | 12 | CHECK ELEVATOR HINGES, HORN AND ATTACHMENTS |  |
|  | 13 | CHECK THAT ELEVATOR TRAVEL IS WITHIN LIMITS UP_______DOWN________ |  |
|  | 14 | CHECK HORIZONTAL STABILIZER ATTACHMENTS |  |
|  | 15 | CHECK HORIZONTAL TRIM FOR INSTALLATION, SECURITY AND OPERATION. CHECK RV10 SERVO PIVOT BOLT SAFETY. |  |
|  | 16 | CHECK AUTOPILOT SERVO INSTALLATION & TT SERVO ARM RETAINER SB |  |
|  | 17 | RE-INSTALL PANELS AND TAIL FAIRING |  |
|  | 18 | VERIFY SERVICE BULLETINS COMPLIANCE |  |
| WING GROUP |  |  |  |
|  | 1. | REMOVE INSPECTION PLATES AND FAIRINGS |  |
|  | 2. | CHECK WING SKINS FOR DAMAGE, DISTORTION, SMOKING OR LOOSE RIVETS, ETC. |  |
|  | 3. | CHECK AILERON HINGES, PUSHRODS FOR OPERATION |  |
|  | 4. | CHECK AUTOPILOT INSTALLATION FOR SECURITY & PROPER INSTALLATION |  |
|  | 5. | CHECK FLAP CONDITION AND SECURITY, LUBRICATE HINGES AND BEARINGS |  |
|  | 6. | CHECK FLAP OPERATION, INSPEC AND CHECK FLAP ACTUATOR AND SAFETY |  |
|  | 7. | CHECK FOR LEAKS AT FUEL TANK ACCESS PLATES, FUEL LEVEL SENSORS |  |
|  | 8. | CHECK SECURITY OF ACTUATOR ROD AND BEARING AT FLAP ATTACH POINT |  |
|  | 9. | CHECK PITOT TUBE AND LINES FOR DAMAGE AND SECURITY |  |
|  | 10 | CHECK WINGTIPS FOR DAMAGE AND SECURITY |  |
|  | 11 | CHECK OPERATION OF LANDING LIGHTS |  |
|  | 12 | CHECK OPERATION OF STROBE LIGHTS |  |
|  | 13 | CHECK OPERATION OF POSITION LIGHTS |  |
|  | 14 | RE-INSTALL INSPECTION PANELS AND FAIRINGS |  |
|  | 15 | INSPECT FUEL TANK INTERNALLY FOR PEELING SEALANT (SLOSH) |  |
|  | 16 | CHECK CONDITION OF FUEL CAPS, O RINGS, AND SUMP DRAINS. |  |
|  | 18 | RE-INSTALL INSPECTION PLATES AND FAIRINGS |  |
| LANDING GEAR |  |  |  |
|  | 1 | PLACE AIRCRAFT ON JACKS |  |
|  | 2. | REMOVE WHEEL PANTS AND GEAR FAIRINGS |  |
|  | 3. | CHECK TIRES FOR WEAR AND DAMAGE |  |
|  | 4. | REMOVE WHEELS INSPECT FOR CRACKS, CORROSION, GENERAL CONDITION |  |
|  | 5. | CHECK TIRE PRESSURES LEFT______NOSE______RIGHT______ |  |
|  | 6. | CHECK BRAKE LININGS AND DISCS FOR WEAR |  |
|  | 7. | CHECK BRAKE LINES, CALIPERS FOR LEAKS, SECURITY AND CONDITION |  |
|  | 8. | CHECK WHEEL FAIRINGS AND MOUNTING PLATES FOR CRACKS AND SECURITY, CHECK ALL BOLTS FOR PROPER SECURITY/TORQUE. |  |
|  | 9. | CLEAN AND LUBRICATE MAIN / NLG / TAIL WHEEL BEARINGS AND BUSHINGS |  |
|  | 10 | RE-INSTALL WHEELS, BRAKES |  |
|  | 11 | REMOVE TAIL WHEEL AND FORK, CLEAN AND LUBRICATE BUSHING / PIN, CHECK LOCKING MECHANISM. |  |
|  | 12 | CHECK NOSE WHEEL BOLTS, BRACKETS, BREAKOUT FORCE, STOP ORIENTATION |  |
|  | 13 | CHECK ALL LANDING GEAR UPPER RETAINING BOLTS FOR PROPER TORQUE |  |
|  | 14 | CHECK BRAKE FLUID LEVEL. TYPE OF FLUID BEING USED__________________ |  |
|  | 15 | INSTALL WHEEL PANTS AND GEAR FAIRINGS |  |
|  | 16 | REMOVE AIRCRAFT FROM JACKS |  |
| OPERATION CHECK |  |  |  |
|  | 1. | CHECK BOOST PUMP PRESSURE |  |
|  | 2. | CHECK ALTERNATOR OUTPUT |  |
|  | 3. | CHECK AVIONIC EQUIPMENT OPERATION |  |
|  | 4. | CHECK OIL PRESSURE |  |
|  | 5. | CHECK MANIFOLD PRESSURE |  |
|  | 6. | CHECK PROPELLER OPERATION AND SMOOTHNESS |  |
|  | 7. | CHECK MAG DROP AT 1800 RPM LEFT______RIGHT______ |  |
|  | 8. | CHECK STATIC R.P.M |  |
|  | 9. | CHECK IDLE R.P.M. |  |
|  | 10 | CHECK MAG SWITCH WIRES FOR GROUNDING |  |
|  | 11 | CHECK THROTTLE AND MIXTURE CONTROL OPERATION |  |
|  | 12 | CHECK IDLE MIXTURE |  |
|  | 13 | LEAK CHECK ENGINE |  |
|  | 14 | RE-INSTALL ENGINE COWLS |  |
|  | 15 | CHECK FLIGHT CONTROL OPERATION (AILERON, ELEVATOR, RUDDER, TRIM) |  |
| GENERAL |  |  |  |
|  | 1. | FINAL CHECK FOR CLEANLINESS, TOOLS REMOVED, ETC. |  |
|  | 2. | AIRCRAFT PAPERS IN PROPER ORDER A. REGISTRATION |  |
|  |  | B. AIRWORTHINESS |  |
|  |  | C. OPERATING LIMITS |  |
|  |  | D. WEIGHT & BALANCE |  |
| NOTES |  |  |  |

SIGNATURE OF INSPECTOR___________________________________________________________________

CERTIFICATE NUMBER________________________________________________________________________

DATE OF SIGN-OFF___________________________________________________________________________